## Slide 1
Spanning Tree Protocol

## Slide 2
Spanning Tree Protocol
10BaseT Ports (12)
100BaseT Ports
10BaseT Ports (12)
100BaseT Ports
A
Redundant Paths and No Spanning Tree. So, what’s the problem?
Moe
Larry
Host Kahn
Host Baran
A
Hub
Cisco Networking Academy Program

## Slide 3
10BaseT Ports (12)
10BaseT Ports (12)
A
Moe
Larry
Host Kahn
Host Baran
A
Hub
100BaseT Ports
100BaseT Ports
Host Kahn sends an Ethernet frame to Host Baran. Both Switch Moe and Switch Larry see the frame and record Host Kahn’s Mac Address in their switching tables.

## Slide 4
10BaseT Ports (12)
10BaseT Ports (12)
100BaseT Ports
A
Moe
Larry
Host Baran
A
SAT (Source Address Table)
Port 1: 00-90-27-76-96-93
SAT (Source Address Table)
Port 1: 00-90-27-76-96-93
1
1 2
00-90-27-76-96-93
00-90-27-76-5D-FE
Hub
Host Kahn

## Slide 5
SAT (Source Address Table)
Port 1: 00-90-27-76-96-93
SAT (Source Address Table)
Port 1: 00-90-27-76-96-93
10BaseT Ports (12)
10BaseT Ports (12)
100BaseT Ports
A
Moe
Larry
A
1
1 2
00-90-27-76-96-93
00-90-27-76-5D-FE
Hub
Both Switches do not have the destination MAC address in their table so they flood it out all ports.
Host Baran
Host Kahn

## Slide 6
SAT (Source Address Table)
Port 1: 00-90-27-76-96-93
10BaseT Ports (12)
10BaseT Ports (12)
100BaseT Ports
A
Moe
Larry
A
1
1 2
00-90-27-76-96-93
00-90-27-76-5D-FE
Hub
SAT (Source Address Table)
Port 1: 00-90-27-76-96-93
Port A: 00-90-27-76-96-93
Switch Moe now learns, incorrectly, that the Source Address
00-90-27-76-96-93 is on Port A.
Host Baran
Host Kahn

## Slide 7
SAT (Source Address Table)
Port 1: 00-90-27-76-96-93
Port A: 00-90-27-76-96-93
SAT (Source Address Table)
Port 1: 00-90-27-76-96-93
Port A: 00-90-27-76-96-93
10BaseT Ports (12)
10BaseT Ports (12)
100BaseT Ports
A
Moe
Larry
A
1
1 2
00-90-27-76-96-93
00-90-27-76-5D-FE
Hub
Switch Larry also learns, incorrectly, that the Source Address 00-90-27-76-96-93 is on Port A.
Host Baran
Host Kahn

## Slide 8
SAT (Source Address Table)
Port A: 00-90-27-76-96-93
10BaseT Ports (12)
10BaseT Ports (12)
100BaseT Ports
A
Moe
Larry
A
1
1 2
00-90-27-76-96-93
00-90-27-76-5D-FE
Hub
SAT (Source Address Table)
Port A: 00-90-27-76-96-93
Now, when Host Baran sends a frame to Host Kahn, it will be sent the longer way, through Switch Larry’s port A.
Host Baran
Host Kahn

## Slide 9
Then the same confusion happens, but this time with Host Baran. Okay, maybe this is not the end of the world. Frames will just take a longer path and you may also see other “unexpected results.”
But what about broadcast frames, like ARP Requests?

## Slide 10
10BaseT Ports (12)
10BaseT Ports (12)
100BaseT Ports
A
Moe
Larry
Host Kahn
A
1
1 2
00-90-27-76-96-93
00-90-27-76-5D-FE
Hub
Lets, leave the switching tables alone and just look at what happens with the frames. Host Kahn sends out a Layer 2 broadcast frame, like an ARP Request.
Host Baran

## Slide 11
10BaseT Ports (12)
10BaseT Ports (12)
100BaseT Ports
A
Moe
Larry
Host Kahn
A
1
1 2
00-90-27-76-96-93
00-90-27-76-5D-FE
Hub
Because it is a Layer 2 broadcast frame, both switches, Moe and Larry, flood the frame out all ports, including their port A’s.
Host Baran

## Slide 12
10BaseT Ports (12)
10BaseT Ports (12)
100BaseT Ports
A
Moe
Larry
Host Kahn
A
1
1 2
00-90-27-76-96-93
00-90-27-76-5D-FE
Hub
Duplicate
frame
Duplicate
frame
Both switches receive the same broadcast, but on a different port. Doing what switches do, both switches flood the duplicate broadcast frame out their other ports.
Host Baran

## Slide 13
10BaseT Ports (12)
10BaseT Ports (12)
100BaseT Ports
A
Moe
Larry
A
1 2
00-90-27-76-96-93
00-90-27-76-5D-FE
Hub
Duplicate
Frame
Duplicate
Frame
Here we go again, with the switches flooding the same broadcast again out its other ports. This results in duplicate frames, known as a broadcast storm!
Host Kahn
Host Baran

## Slide 14
10BaseT Ports (12)
10BaseT Ports (12)
A
Moe
Larry
A
1 2
00-90-27-76-96-93
00-90-27-76-5D-FE
Hub
Remember, that Layer 2 broadcasts not only take up network bandwidth, but must be processed by each host. This can severely impact a network, to the point of making it unusable.
Host Kahn
Host Baran

## Slide 15
Spanning Tree to the Rescue!

## Slide 16
Broadcast Frame
Standby Link
Switches forward broadcast frames
Prevents loops
Loops can cause broadcast storms, exponentially proliferate frames
Allows redundant links
Prunes topology to a minimal spanning tree
Resilient to topology changes and device failures
Main function of the Spanning Tree Protocol (STP) is to allow redundant switched/bridged paths without suffering the effects of loops in the network
Introducing Spanning-Tree Protocol

## Slide 17
The STA is used to calculate a loop-free path.
Spanning-tree frames called bridge protocol data units (BPDUs) are sent and received by all switches in the network at regular intervals and are used to determine the spanning tree topology.
A separate instance of STP runs within each configured VLAN.
(VLANs are later)

## Slide 18
States initially set, later modified by STP
Server ports can be configured to
immediately enter STP forward mode
Understanding STP States
Blocking
Listening
Learning
Forwarding
Disabled

## Slide 19
  Blocking - No frames forwarded, BPDUs heard
  Listening - No frames forwarded, listening for frames
  Learning - No frames forwarded, learning addresses
  Forwarding - Frames forwarded, learning addresses
  Disabled - No frames forwarded, no BPDUs heard
Understanding STP States

## Slide 20
Part of 802.1d standard
Simple principle: Build a loop-free tree from some identified point known as the root.
Redundant paths allowed, but only one active path.
Developed by Radia Perlman
Spanning Tree Algorithm (STA)

## Slide 21
Spanning Tree Process
Step 1: Electing a Root Bridge
Step 2: Electing Root Ports
Step 3: Electing Designated Ports
All switches send out Configuration Bridge Protocol Data Units (Configuration BPDU’s)
BPDU’s are sent out all interfaces every two seconds (by default - tunable)
All ports are in Blocking Mode during the initial Spanning Tree is process.

## Slide 23
Spanning Tree Algorithm (STA):
Bridge Protocol Data Units Fields (BPDU) (FYI)
The fields used in the STA BPDU are provided for your information only.
During the discussion of STA you may wish to refer to this protocol to see how the information is sent and received.

## Slide 24
Protocol Identifier (2 bytes), Version (1 byte), Message Type (1 byte): Not really utilized (N/A here)
Flags (1 byte): Used with topology changes (N/A here)
Root ID (8 bytes): Indicates current Root Bridge on the network, includes:
    Bridge Priority (2 bytes)
    Bridge MAC Address (6 bytes)
    Known as the Bridge Identifier of the Root Bridge

## Slide 25
Cost to Root (4 bytes): Cost of the path from the bridge sending the BDPU to the Root Bridge indicated in the Root ID field. Cost is based on bandwidth.
Bridge ID (8 bytes): Bridge sending the BDPU
  2 bytes: Bridge Priority
  6 bytes: MAC Address
Port ID (2 bytes): Port on bridge sending BDPU, including Port Priority value

## Slide 26
Message Age (2 bytes): Age of BDPU (N/A here)
Maximum Age (2 bytes): When BDPU should be discarded (N/A here)
Hello Time (2 bytes): How often BDPU’s are to be sent (N/A here)
Forward Delay (2 bytes): How long bridge should remain in listening and learning states (N/A here)

## Slide 27
A B
A B
A B
1
1
Moe
Larry
Curly
10BaseT Ports (12)
10BaseT Ports (24)
10BaseT Ports (24)
100BaseT Ports
100BaseT Ports
100BaseT Ports
3 Switches with redundant paths Can you find them?

## Slide 28
3 Steps to Spanning Tree
Step 1: Electing a Root Bridge
  Bridge Priority
  Bridge ID
  Root Bridge
Step 2: Electing Root Ports
  Path Cost or Port Cost
  Root Path Cost
  Root Port
Step 3: Electing Designated Ports
  Path Cost or Port Cost
  Root Path Cost

## Slide 29
Step 1: Electing a Root Bridge
The first step is for switches to select a Root Bridge.
The root bridge is the bridge from which all other paths are decided.
Only one switch can be the root bridge.
Election of a root bridge is decided by:
1. Lowest Bridge Priority
2. Lowest Bridge ID (tie-breaker)

## Slide 30
Bridge Priority
This is a numerical value.
The switch with the with the lowest bridge priority is the root bridge.
The switches use BPDU’s to accomplish this.
All switches consider themselves as the root bridge until they find out otherwise.
All Cisco Catalyst switches have the default Bridge priority of 32768.
It’s a tie! So then what?

## Slide 31
A B
A B
A B
1
1
Moe
Larry
Curly
10BaseT Ports (12)
10BaseT Ports (24)
10BaseT Ports (24)
100BaseT Ports
100BaseT Ports
100BaseT Ports
Bridge Priorities

## Slide 32
Switch Moe: Bridge Priority

## Slide 33
In case of a tie, the Bridge ID is used…
Bridge ID
The Bridge ID is the MAC address assigned to the individual switch.
The lower Bridge ID (MAC address) is the tiebreaker.
Because MAC addresses are unique, this ensures that only one bridge will have the lowest value.
NOTE: There are other tie breakers, if these values are not unique, but we will not cover those situations.

## Slide 35
A B
A B
A B
1
1
Moe
Larry
Curly
10BaseT Ports (12)
10BaseT Ports (24)
10BaseT Ports (24)
100BaseT Ports
100BaseT Ports
Priority: 32768 ID: 00-B0-64-26-6D-00
Priority: 32768 ID: 00-B0-64-58-CB-80
Priority: 32768 ID: 00-B0-64-58-DC-00
Bridge Priorities and Bridge Ids
Which one is the lowest?

## Slide 36
A B
A B
1
1
Moe
Larry
Curly
10BaseT Ports (12)
10BaseT Ports (24)
10BaseT Ports (24)
100BaseT Ports
Priority: 32768 ID: 00-B0-64-26-6D-00
Priority: 32768 ID: 00-B0-64-58-CB-80
Priority: 32768 ID: 00-B0-64-58-DC-00
Lowest: Moe becomes the root bridge
You got it!
A B

## Slide 37
Step 2: Electing Root Ports
After the root bridge is selected, switches (bridges) must locate redundant paths to the root bridge and block all but one of these paths.
The switches use BPDU’s to accomplish this.
How does the switch make the decision on which port to use, known as the root port, and which one should be blocked?

## Slide 38
A B
A B
1
1
Moe
Larry
Curly
10BaseT Ports (12)
10BaseT Ports (24)
10BaseT Ports (24)
100BaseT Ports
Priority: 32768 ID: 00-B0-64-26-6D-00
Priority: 32768 ID: 00-B0-64-58-CB-80
Priority: 32768 ID: 00-B0-64-58-DC-00
?
?
?
?
Redundant Paths
100BaseT Ports
100BaseT Ports
A B

## Slide 39
Path Cost (or Port Cost)
Port Cost is used to help find the “cheapest” or “fastest” path to the root bridge.
By default, port cost is usually based on the medium or bandwidth of the port.
On Cisco Catalyst switches, this value is derived by dividing 1000 by the speed of the media in megabits per second.
Examples:
Standard Ethernet: 1,000/10 = 100
Fast Ethernet: 1,000/100 = 10

## Slide 40
Root Path Cost
The root path cost is the cumulative port costs (path costs) to the Root Bridge.
This value is transmitted in the BPDU cost field.

## Slide 41
However, everything is viewed in relation to the root bridge.
Root Ports
Ports directly connected to the root bridge will be the root ports.
Otherwise, the port with the lowest root path cost will be the root port.

## Slide 42
A B
A B
1
1
Moe
Larry
Curly
10BaseT Ports (12)
10BaseT Ports (24)
10BaseT Ports (24)
100BaseT Ports
Priority: 32768 ID: 00-B0-64-26-6D-00
Priority: 32768 ID: 00-B0-64-58-CB-80
Priority: 32768 ID: 00-B0-64-58-DC-00
100
10
10
10
Path Costs
100BaseT Ports
100BaseT Ports
A B

## Slide 43
Curly
Even though the Path Cost to the root bridge for Curly is higher using Port 1, Port 1 has a direct connection to the root bridge, thus it becomes the root port.
Port 1 is then put in Forwarding mode, while the redundant path of Port A, is put into Blocking mode.

## Slide 44
A B
A B
1
1
Moe
Larry
Curly
10BaseT Ports (12)
10BaseT Ports (24)
10BaseT Ports (24)
100BaseT Ports
Priority: 32768 ID: 00-B0-64-26-6D-00
Priority: 32768 ID: 00-B0-64-58-CB-80
Priority: 32768 ID: 00-B0-64-58-DC-00
X Blocking
Forwarding
100BaseT Ports
100BaseT Ports
Curly
A B

## Slide 45
Larry
Larry also has a root port, a direct connection with the root bridge, through Port B.
Port B is then put in Forwarding mode, while the redundant path of Port A, is put into Blocking mode.

## Slide 46
A B
A B
1
1
Moe
Larry
Curly
10BaseT Ports (12)
10BaseT Ports (24)
10BaseT Ports (24)
100BaseT Ports
Priority: 32768 ID: 00-B0-64-26-6D-00
Priority: 32768 ID: 00-B0-64-58-CB-80
Priority: 32768 ID: 00-B0-64-58-DC-00
X Blocking
Forwarding
100BaseT Ports
100BaseT Ports
X Blocking
Forwarding
A B
Larry

## Slide 47
A B
A B
1
1
Moe
Larry
Curly
10BaseT Ports (12)
10BaseT Ports (24)
10BaseT Ports (24)
100BaseT Ports
Priority: 32768 ID: 00-B0-64-26-6D-00
Priority: 32768 ID: 00-B0-64-58-CB-80
Priority: 32768 ID: 00-B0-64-58-DC-00
X Blocking
100BaseT Ports
100BaseT Ports
X Blocking
A B
Root Port
Root Port
Root Ports

## Slide 48
Step 3: Electing Designated Ports
The single port for a switch that sends and receives traffic to and from the Root Bridge.
It can also be thought of as the port that is advertising the lowest cost to the Root Bridge.
In our example, we only have the two obvious choices, which are on switch Moe.
If we had other LAN segments, we could explain designated ports in more detail, but this is fine for now.

## Slide 49
A B
A B
1
1
Moe
Larry
Curly
10BaseT Ports (12)
10BaseT Ports (24)
10BaseT Ports (24)
Priority: 32768 ID: 00-B0-64-26-6D-00
Priority: 32768 ID: 00-B0-64-58-CB-80
Priority: 32768 ID: 00-B0-64-58-DC-00
X Blocking
Forwarding
100BaseT Ports
100BaseT Ports
X Blocking
Forwarding
A B
Designated Port
Designated Port
Designated Ports

## Slide 50
Spanning Tree is now complete, and the switches
can begin to properly switch frames out the proper
ports with the correct switching tables and without
creating duplicate frames.

## Slide 51
Most LAN and switched internetwork books provide information on Spanning Tree. For more complex examples, you may wish to try these books:
Cisco Catalyst LAN Switching, by Rossi and Rossi, McGraw Hill (Very Readable)
CCIE Professional Development: Cisco LAN Switching, by Clark and Hamilton, Cisco Press (More Advanced)
Interconnections, by Radia Perlman, Addison Wesley (Excellent, but very academic)

## Slide 52
Extra Item!
Port Fast Mode (from Cisco documentation)
Port Fast mode immediately brings a port from the blocking state into the forwarding state by eliminating the forward delay (the amount of time a port waits before changing from its STP learning and listening states to the forwarding state).

## Slide 53
When the switch is powered up, the forwarding state, even if Port Fast mode is enabled, is delayed to allow the Spanning-Tree Protocol to discover the topology of the network and ensure no temporary loops are formed.
Spanning-tree discovery takes approximately 30 seconds to complete, and no packet forwarding takes place during this time.
After the initial discovery, Port Fast-enabled ports transition directly from the blocking state to the forwarding state.

## Slide 54
A B
A B
1
1
Moe
Larry
Curly
10BaseT Ports (12)
10BaseT Ports (24)
10BaseT Ports (24)
100BaseT Ports
Priority: 32768 ID: 00-B0-64-26-6D-00
Priority: 32768 ID: 00-B0-64-58-CB-80
Priority: 32768 ID: 00-B0-64-58-DC-00
X Blocking
Forwarding
100BaseT Ports
100BaseT Ports
X Blocking
Forwarding
A B
Spanning Tree Completed

## Slide 55
Moe- Port 1

## Slide 56
Moe- Port B

## Slide 57
Larry

## Slide 58
Larry- Port 1

## Slide 59
Larry- Port B

## Slide 60
Curly

## Slide 61
Curly- Port 1

## Slide 62
Curly- Port A

## Slide 63
First , the root must be selected.
By ID, it is elected.
Least cost paths from root are traced.
In the tree, these paths are placed.
A mesh is made by folks like me,
Then bridges find a spanning tree.
I think that I shall never see
A graph more lovely than a tree.
A tree whose crucial property
Is loop-free connectivity.
A tree that must be sure to span.
So packets can reach every LAN.
The Spanning Tree Algorhyme by Radia Perlman