## Slide 1: Configuring CME Additional Features
Cisco Networking Academy Program

## Slide 2: Cisco CME GUI Features
Notes: <number>
Thanks for joining us today to attend the Cisco Brand and Corporate Identity Workshop.
In the first half of the workshop I am going to cover Brand Matters and talk in detail about the Cisco brand, and in the second half my colleague Gary McCavvit is going to take you through our updated visual identity system.
At the end of the workshop we’re going to leave some time for a fun quiz as well as some Q&A.

## Slide 3: User Classes
Cisco CME provides three levels of HTTP based GUI access:
  System Administrator
  Customer Administrator
  Phone User
Notes: <number>

## Slide 4: User Classes (Cont.)
System and Customer Administrator Web-based GUI interface
HTTP://ip_address/ccme.html
Notes: <number>

## Slide 5: User Classes (Cont.)
Phone User GUI Web interface
Notes: <number>

## Slide 6: Cisco CallManager Express GUI Prerequisites
Ensure the proper files are in flash on the Cisco CallManager router
Configure and enable the HTTP server on the router
HTTP Server Authentication Method (Optional)
Configure System Administrator Credentials
The following tasks should be completed before the GUI is available
Notes: <number>

## Slide 7: Cisco CallManager Express GUI Prerequisites (Cont.)
ip http server
router(config)#
ip http path flash:
router(config)#
ip http authentication {aaa | enable | local | tacacs}
router(config)#
Enables the HTTP server on the router
Sets the http server path to the flash memory
Determines the method type of authentication used by the HTTP Server

## Slide 8: Cisco CallManager Express GUI Prerequisites (Cont.)
telephony-service
router(config)#
web admin system name username {password string | secret {0 | 5} string}
router(config-telephony-service)#
Enters telephony-service configuration mode
Sets a username and password for the GUI system administrator

## Slide 9: Cisco CallManager Express GUI Prerequisites (Cont.)
dn-webedit
router(config-telephony-service)#
(Optional) Enables the ability to add ephone directory numbers through the CallManager Express GUI
time-webedit
router(config-telephony-service)#
(Optional) Enables the ability to set the system time through the CallManager Express GUI

## Slide 10: Accessing the GUI
The GUI in CallManager Express is Web-based
Use IE 6.0 or greater
Use the URL
  Hyperlink: http://router_ipaddr/ccme.html
Enter either system admin, customer admin or phone user credentials when prompted
Notes: <number>

## Slide 11: Configuring Administrative User Classes
Create and load a custom XML configuration file
Define the customer administrator credentials
To configure a customer administrator with a subset of the system administrator access, two steps must be taken:
Notes: <number>

## Slide 12: Configuring Administrative User Classes (Cont.)
Step 1 - Open a copy of the xml.template file in a text editor
Step 2 - Edit the file with desired changes to access
Step 3 - Save the file with a desired name
Step 4 - Upload to flash on the CallManager Express router via TFTP or FTP
Step 5 - Load the template from flash to the RAM on the CallManager Express router
Creating and loading an XML configuration file is a five step process
Notes: <number>

## Slide 13: Configuring Administrative User Classes (Cont.) – Demonstration
  Step 1 – Copy of xml.template in text editor
<Presentation>
<MainMenu>
<!-- Take Higher Precedence over CLI "dn-web-edit" -->
<AddExtension> [Hide | Show] </AddExtension>
<DeleteExtension> [Hide | Show] </DeleteExtension>
<AddPhone> [Hide | Show] </AddPhone>
<DeletePhone> [Hide | Show] </DeletePhone>
</MainMenu>
<Extension>
<!--Control both view and change, and possible add or delete-->
<SequenceNumber> [Hide | Show] </SequenceNumber>
<Type> [Hide | Show] </Type>
<Huntstop> [Hide | Show] </Huntstop>
<Preference> [Hide | Show] </Preference>
<HoldAlert> [Hide | Show] </HoldAlert>
<TranslationRules> [Hide | Show] </TranslationRules>
<Paging> [Hide | Show] </Paging>
<Intercom> [Hide | Show] </Intercom>
<MWI> [Hide | Show] </MWI>
<MoH> [Hide | Show] </MoH>
<LBDN> [Hide | Show] </LBDN>
<DualLine> [Hide | Show] </DualLine>
<Reg> [Hide | Show] </Reg>
<PGroup> [Hide | Show] </PGroup>
…

## Slide 14: Configuring Administrative User Classes (Cont.) – Demonstration
  Step 2 - xml.template in text editor
<Presentation>
<MainMenu>
<AddExtension> Hide </AddExtension>
<DeleteExtension> Hide </DeleteExtension>
<AddPhone> Show </AddPhone>
<DeletePhone> Show </DeletePhone>
</MainMenu>
<Extension>
<SequenceNumber> Hide </SequenceNumber>
<Type> Hide </Type>
<Huntstop> Hide </Huntstop>
<Preference> Hide </Preference>
<HoldAlert> Hide </HoldAlert>
<TranslationRule> Hide </TranslationRule>
<Paging> Show </Paging>
<Intercom> Hide </Intercom>
<MWI> Hide </MWI>
<MoH> Hide </MoH>
<LBDN> Hide </LBDN>
<DualLine> Hide </DualLine>
<Reg> Hide </Reg>
<PGroup> Hide </PGroup>
</Extension>
…

## Slide 15: Configuring Administrative User Classes (Cont.) – Demonstration Results
Modified XML Template applied
Default system Administrator access
Notes: <number>

## Slide 16: Configuring Administrative User Classes (Cont.)
Define the custom administrator credentials in one of two ways:
  Through the System Administrator GUI
  From the CLI of the CallManager Express
Notes: <number>

## Slide 17: Configuring Administrative User Classes (Cont.)
To add a Customer Admin
  Add a username
  Select Customer from the Admin type
  Set the password
Notes: <number>

## Slide 18: Configuring Administrative User Classes (Cont.)
telephony-service
router(config)#
Enters telephony-service configuration mode
web admin customer name username password string
router(config-telephony-service)#
Sets a username and password for the GUI customer administrator

## Slide 19: Configuring Administrative User Classes (Cont.)
Two ways to define phone users:
  Through the System Administrator GUI
  From the CLI of the CallManager Express
Notes: <number>

## Slide 20: Configuring Administrative User Classes (Cont.)
Select the phone of the user, then set credentials on the phone
Notes: <number>

## Slide 21: Configuring Administrative User Classes (Cont.)
ephone phone tag
router(config)#
Enters telephony-service configuration mode
username username password password
router(config-ephone)#
Sets a username and password for the GUI phone user

## Slide 22: Configuring Phone Features
Notes: <number>
Thanks for joining us today to attend the Cisco Brand and Corporate Identity Workshop.
In the first half of the workshop I am going to cover Brand Matters and talk in detail about the Cisco brand, and in the second half my colleague Gary McCavvit is going to take you through our updated visual identity system.
At the end of the workshop we’re going to leave some time for a fun quiz as well as some Q&A.

## Slide 23: Call Transfer Transferring a Call from an IP Phone
User transfers a call to another DN
Notes: <number>

## Slide 24: Call Transfer (Cont.) Configuring
Call Transfer Commands
  Configuring system transfer settings
  Configuring individual IP phone transfer settings
  Configuring a transfer pattern
Notes: <number>

## Slide 25: Call Transfer (Cont.) Configuring
transfer-system {blind | full-blind | full-consult | local-consult}
router(config-telephony-service)#
CMERouter(config-telephony-service)#transfer-system full-blind
Specifies the call transfer method for all Cisco CME extensions

## Slide 26: Call Transfer (Cont.) Configuring
transfer-mode {blind | consult}
router(config-ephone-dn)#
CMERouter(config-ephone-dn)#transfer-mode consult
Specifies the type of call transfer for an individual IP phone extension number

## Slide 27: Call Transfer (Cont.) Configuring
transfer-pattern transfer-pattern [blind]
router(config-telephony-service)#
CMERouter(config-telephony-service)#transfer-pattern 2095559... blind
To allow transfer of telephone calls from Cisco IP phones to phones other than Cisco IP phones

## Slide 28: Call Forwarding Forwarding a Call from an IP phone
User forwards all calls to a DN
Notes: <number>

## Slide 29: Call Forwarding (Cont.) Forwarding a Call from an IP phone
Forward all, busy, and no answer all in the phone user Web pages
Notes: <number>

## Slide 30: Call Forwarding (Cont.) Configuring
Call Forwarding Commands
Call forward all
Call forward busy
Call forward no answer
Call forward max-length
Call forward pattern
Notes: <number>

## Slide 31: Call Forwarding (Cont.) Configuring
call-forward all directory-number
CMERouter(config-ephone-dn)#
Forwards all calls to the Directory Number specified
call-forward busy directory-number
CMERouter(config-ephone-dn)#
Forwards incoming calls when the DN is busy to another DN
call-forward noan directory-number timeout seconds
CMERouter(config-ephone-dn)#
Forwards calls that are not answered in the time specified to another DN

## Slide 32: Call Forwarding (Cont.) Configuring
call-forward max-length length
CMERouter(config-ephone-dn)#
Restricts the number of digits that can be used with call forward
call-forward pattern pattern
CMERouter(config-telephony-service)#
To specify a pattern for calling-party numbers that support H.450.3

## Slide 33: IP Phone Display Configuring
IP Phone Header Bar
System Text Message
System Display Message (Idle URL)
The Phone display can be customized in the following ways
Notes: <number>

## Slide 34: IP Phone Display (Cont.)
System Text Message
IP Phone Header Bar
System Display Message
Label
Notes: <number>

## Slide 35: IP Phone Display (Cont.)
ephone-dn dn-tag
CMERouter(config)#
Enters ephone-dn configuration mode
description display-text
CMERouter(config-ephone-dn)#
Enters the header bar for the IP Phone
IP Phone Header Bar
label string
CMERouter(config-ephone-dn)#
Configures a label on the line instead of the line number

## Slide 36: IP Phone Display (Cont.)
system message text-message
CMERouter(config-telephony-service)#
Sets the text message to play when the phone is idle
url idle url idle-timeout seconds
CMERouter(config-telephony-service)#
Sets a url to be displayed on the IP phone when idle for the set number of seconds
System Display Message (Idle URL)

## Slide 37: IP Phone Display (Cont.)
url {directory | services} url
CMERouter(config-telephony-service)#
Sets the url that will be used when the corresponding function button is pressed
Provisioning URL for customized function buttons
telephony-service
url directories http://10.4.212.11/localdirectory
url services http://10.4.212.4/CCMUser/123456/urltest.html

## Slide 38: Calling and Directory Features
Directory can be accessed by pressing the directory button
Notes: <number>

## Slide 39: Calling and Directory Features (Cont.)
The directory can be accessed through the phone user Web page
HTTP://ip_address/ccme.html
Notes: <number>

## Slide 40: Calling and Directory Features (Cont.)
Adding a user to the directory of CallManager Express
Notes: <number>

## Slide 41: Calling and Directory Features (Cont.)
Notes: <number>

## Slide 42: Calling and Directory Features (Cont.)
directory {first-name-first | last-name-first}
router(config-telephony-service)#
Sets the order that the directory will be listed in
directory entry {[entry-tag number name name] | clear}
router(config-telephony-service)#
Sets the order that the directory will be listed in
Directory order and entry
name name
router(config-ephone-dn)#
Associates a name with an extension (ephone-dn)

## Slide 43: Productivity Tools
Productivity tools for Cisco CME include:
  Flash softkey for hookflash functionality
  Intercom
  Paging
Notes: <number>

## Slide 44: Productivity Tools (Cont.)
fxo hook-flash
router(config-telephony-service)#
Enables the flash softkey button on the IP phones
Flash Softkey for Hookflash Functionality

## Slide 45: Productivity Tools (Cont.)
ephone-dn 10
number 1100
name “Admin Assistant”
ephone-dn 20
number 1199
name “The Boss”
ephone-dn 51
number B5000
name “Admin Assistant”
intercom B4999 label “Admin Assist”
ephone-dn 52
number B4999
name “The Boss”
intercom B5000 label “The Boss”
ephone 6
button 1:10 2:51
ephone 7
button 1:20 2:52
Phone A – The Boss
Line 1 – 1100
Line 2 – Admin Assist
Phone B – Admin Assistant
Line 1 – 1199
Line 2 – The Boss
Intercom
Notes: <number>

## Slide 46: Productivity Tools (Cont.)
intercom extension-number [barge-in | no-auto-answer] [label label]
router(config-ephone-dn)#
Programs an extension to call another intercom phone
Intercom

## Slide 47: Productivity Tools (Cont.)
Paging Function
  Creates a one way voice path
  Unicast or Multicast
  Single Group
  Multiple Groups
Notes: <number>

## Slide 48: Productivity Tools (Cont.)
Single Paging Group
ephone 1
paging Group 4
ephone 2
paging Group 4
Phone dials 4444
ephone-dn 4
number 4444
name Paging Shipping
paging ip 239.0.1.20 port 2000
ephone-dn 21
number 2121
ephone-dn 22
number 2222
ephone 1
mac-address 3662.0234.6ae2
button 1:21
paging-dn 4
ephone 2
mac-address 9387.6738.2873
button 1:22
paging-dn 4
Notes: <number>

## Slide 49: Productivity Tools (Cont.)
Paging DN set up by adding a new extension through the GUI
Assign the paging extension to the phone

## Slide 50: Productivity Tools (Cont.)
paging [ip multicast-address port udp-port]
router(config-ephone-dn)#
Configures the ephone-dn as paging extension using either unicast or multicast
paging-dn paging-dn-tag [unicast]
router(config-ephone)#
Creates a paging extension to receive audio pages on the ephone
Paging Commands

## Slide 51: Productivity Tools (Cont.)
ephone-dn 10
number 2000
name Tech Support
paging ip 239.0.1.20 port 2000
ephone-dn 20
number 2001
name Sales Dept
paging ip 239.0.1.21 port 2000
ephone-dn 22
number 2002
paging ip 239.0.2.22 port 2000
paging group 10,20
ephone 1
paging-group 10
ephone 2
paging-group 10
ephone 3
paging-group 20
ephone 4
paging-group 20
ephone 1
paging Group 10
ephone 2
paging Group 10
ephone 3
paging Group 20
ephone 4
paging Group 20
Phone dials 2000, 2001 or 2002
Combined Paging Group
  Phone dials 2000 and phone 1 and phone 2 get page
  Phone dials 2001 and phone 3 and phone 4 get page
  Phone dials 2002 and all 4 phones get page
Notes: <number>

## Slide 52: Productivity Tools (Cont.)
paging-group paging-dn-tag, paging-dn-tag,…
router(config-ephone-dn)#
Creates a combined paging group from two or more previously defined paging directory numbers
Paging Group

## Slide 53: Custom IP Phone Rings
To create custom rings for IP phones follow these steps:
  Step 1 - Create a ring in the form of a raw PCM file
  Step 2 - Create a RingList.xml file using a text editor to point to the various rings that are desired
  Step 3 - Load the rings and RingList.xml file to flash on the CallManager Express router
  Step 4 - Configure the tftp server to serve up the rings and RingList.xml
  Step 5 - Reboot the phones
Notes: Timeouts interdigit
This task configures the interdigit timeout value for all Cisco IP phones. The interdigit timeout is the amount of time that can elapse between the dialing of digits before the dialing process times out and is terminated.
Timeouts ringing
The ringing timeout is the amount of time a phone can ring with no answer before returning a disconnect code to the caller. This timeout is used only for extensions that do not have no-answer call forwarding enabled. The ringing timeout prevents hung calls received over interfaces such as Foreign Exchange Office (FXO) that do not have forward-disconnect supervision.

## Slide 54: Music on Hold
Music on Hold (MoH) can be derived from two sources:
  Audio file in .wav or .au format
  Live audio source via a feed
Notes: <number>

## Slide 55: Music on Hold (Cont.)
Phone on Hold
Phone on Hold
Flash:
MyMohfile.wav
unicast or multicast
Configuring MoH from file
telephony-service
moh MyMoHfile.wav
multicast moh 239.23.4.10 port 2000
Notes: <number>

## Slide 56: Music on Hold (Cont.)
moh filename
router(config-telephony-service)#
Configures MoH using the file specified in flash
multicast moh ip-address port port-number [route ip-address-list]
router(config-telephony-service)#
(Optional) Specifies that the MoH file should be multicast using the parameters specified
Configuring MoH from file

## Slide 57: Music on Hold (Cont.)
Phone on Hold
Phone on Hold
unicast or multicast
E&M port - 4-wire, immediate start, auto-cut through
Configuring MoH from a live source
voice-port 1/1/1
auto-cut-through
operation 4-wire
signal immediate
dial-peer 7777 voice pots
destination-pattern 7777
port 1/1/1
ephone-dn 12
number 9999
moh out-call 7777
E&M port 1/1/1
Notes: <number>

## Slide 58: Music on Hold (Cont.)
voice-port port
CMERouter(config)#
Enters voice port config mode for the E&M port
input gain decibels
CMERouter(config-voice-port)#
(Optional) sets gain on the MoH signal
Configuring MoH from a live source
auto-cut-through
CMERouter(config-voice port)#
Enables call completion when no M-lead response is sent

## Slide 59: Music on Hold (Cont.)
operation 4-wire
CMERouter(config-voice-port)#
Sets the E&M port to use a 4-wire scheme
signal immediate
CMERouter(config-voice-port)#
Directs calling side to seize the E-lead and send DTMF digits
Configuring MoH from a live source

## Slide 60: Music on Hold (Cont.)
dial-peer voice tag pots
CMERouter(config)#
Creates the dial peer for the MOH connection
port port
CMERouter(config-dial-peer)#
Associates the voice port to the dial peer
Configuring MoH from a live source
destination-pattern string
CMERouter(config-dial-peer)#
Specifies the DN of the MoH source

## Slide 61: Music on Hold (Cont.)
ephone-dn tag
CMERouter(config)#
Creates an ephone-dn
number number
CMERouter(config-ephone-dn)#
Configures a dummy DN for this ephone-dn instance
Configuring MoH from a live source
moh [out-call outcall-number]
CMERouter(config-ephone-dn)#
Specifies this ephone-dn is used for an incoming or outgoing call that is to be the source for a MOH stream