## Slide 1: Improving and Maintaining Voice Quality
Cisco Networking Academy Program

## Slide 2: IP QoS Mechanisms
Notes: Thanks for joining us today to attend the Cisco Brand and Corporate Identity Workshop.
In the first half of the workshop I am going to cover Brand Matters and talk in detail about the Cisco brand, and in the second half my colleague Gary McCavvit is going to take you through our updated visual identity system.
At the end of the workshop we’re going to leave some time for a fun quiz as well as some Q&A.

## Slide 3: QoS Mechanisms
Classification: Each class-oriented QoS mechanism has to support some type of classification
Marking: Used to mark packets based on classification and/or metering
Congestion Management: Each interface must have a queuing mechanism to prioritize transmission of packets
Traffic Shaping: Used to enforce a rate limit based on the metering by delaying excess traffic
Compression: Reduces serialization delay and bandwidth required to transmit data by reducing the size of packet headers or payloads
Link Efficiency: Used to improve bandwidth efficiency through compression and link fragmentation and interleaving

## Slide 4: Classification
Classification is the identifying and splitting of traffic into different classes
Traffic can be classed by various means including the DSCP
Modular QoS CLI allows classification to be implemented separately from policy

## Slide 5: Marking
Marking, which is also known as coloring, marks each packet as a member of a network class so that the packet’s class can be quickly recognized throughout the rest of the network

## Slide 6: Trust Boundaries Classify Where?
Cisco’s QoS model assumes that the CoS carried in a frame may or may not be trusted by the network device
For scalability, classification should be done as close to the edge as possible
End hosts can mostly not be trusted to tag a packet’s priority correctly
The outermost trusted devices represent the trust boundary
1 and 2 are optimal, 3 is acceptable (if access switch cannot perform classification)
1
2
3

## Slide 7: Trust Boundaries Mark Where?
For scalability, marking should be done as close to the source as possible
Notes: Classification should take place at the network edge, typically in the wiring closet or within video endpoints or IP phones themselves. The slide demonstrates this with an IP telephony example. Packets can be marked as important by using Layer 2 Class of Service (CoS) settings in the User Priority bits of the 802.1p portion of the 802.1p/Q field or the IP Precedence/Differentiated Services Code Point (DSCP) bits in the ToS/DS field in the IPv4 header. Cisco IP Phones can mark voice packets as high priority using CoS as well as ToS. By default, the phone sends 802.1p tagged packets with the CoS and ToS set to a value of 5.
Because most PCs do not have an 802.1Q capable network interface card (NIC), they send the packets untagged. This means that the frames do not have a 802.1p field. Also, unless the applications running on the PC send packets with a specific CoS value, this field is zero. A special case is where the TCP/IP stack in the PC has been modified to send all packets with a ToS value other than zero. Typically this does not happen, and the ToS value is zero.
Even if the PC is sending tagged frames with a specific CoS value, Cisco IP Phones can zero out this value before sending the frames to the switch. This is the default behavior. Frames coming from the phone have a CoS of 5 and frames coming from the PC have a CoS of 0. When the switch receives these frames, it can take into account these values for further processing based on its capabilities.
The switch uses its queues (available on a per-port basis) to buffer incoming frames before sending them to the switching engine (it is important to remember that input queuing comes into play only when there is congestion). The switch uses the CoS value(s) to put the frames in appropriate queues. The switch can also employ mechanisms such as weighted random early detection (WRED) to make intelligent drops within a queue (also known as congestion avoidance) and weighted round-robin (WRR) to provide more bandwidth to some queues than to others (also known as congestion management).

## Slide 8: Connecting the IP Phone
802.1Q trunking between the switch and IP phone for multiple VLAN support (separation of voice/data traffic) is preferred
The 802.1Q header contains the VLAN information and the CoS 3-bit field, which determines the priority of the packet
For most Cisco IP phone configurations, traffic sent from the IP phone to the switch is trusted to ensure that voice traffic is properly prioritized over other types of traffic in the network
The trusted boundary feature uses CDP to detect an IP phone and otherwise disables the trusted setting on the switch port to prevent misuse of a high-priority queue

## Slide 9: Congestion Management
Congestion management uses the marking on each packet to determine which queue to place packets in
Congestion management utilizes sophisticated queuing technologies such as Weighted Fair Queuing (WFQ) and Low Latency Queuing (LLQ) to ensure that time-sensitive packets like voice are transmitted first

## Slide 10: Shaping
Shaping queues packets when a pre-defined limit is reached

## Slide 11: Compression
Header compression can dramatically reduce the overhead associated with voice transport

## Slide 12: Link Fragmentation and Interleaving
Without Link Fragmentation and Interleaving, time-sensitive voice traffic can be delayed behind long, non-time-sensitive data packets
Link Fragmentation breaks long data packets apart and interleaves time-sensitive packets so that they are not delayed

## Slide 13: Implementing AutoQoS
Notes: Thanks for joining us today to attend the Cisco Brand and Corporate Identity Workshop.
In the first half of the workshop I am going to cover Brand Matters and talk in detail about the Cisco brand, and in the second half my colleague Gary McCavvit is going to take you through our updated visual identity system.
At the end of the workshop we’re going to leave some time for a fun quiz as well as some Q&A.

## Slide 14: AutoQoS
One command per interface to enable and configure QoS

## Slide 15: AutoQoS (Cont.)
interface Multilink1
ip address 10.1.61.1 255.255.255.0
ip tcp header-compression iphc-format
load-interval 30
service-policy output QoS-Policy
ppp multilink
ppp multilink fragment-delay 10
ppp multilink interleave
multilink-group 1
ip rtp header-compression iphc-format
!
interface Serial0
bandwidth 256
no ip address
encapsulation ppp
no ip mroute-cache
load-interval 30
no fair-queue
ppp multilink
multilink-group 1
interface Serial0
  bandwidth 256
  ip address 10.1.61.1 255.255.255.0
  auto qos voip
AutoQoS
Manual QoS

## Slide 16: AutoQoS (Cont.)
Application Classification
  Automatically discovers applications and provides appropriate QoS treatment
Policy Generation
  Automatically generates initial an ongoing QoS policies
Configuration
  Provides high level business knobs, and multi-device / domain automation for QoS
Monitoring & Reporting
  Generates intelligent, automatic alerts and summary reports
Consistency
  Enables automatic, seamless interoperability among all QoS features and parameters across a network topology – LAN, MAN, and WAN

## Slide 17: AutoQoS: Router Platforms
Cisco 1760, 2600, 3600, 3700 and 7200 Series Routers
User can meet the voice QoS requirements without extensive knowledge about:
  Underlying technologies (ie: PPP, FR, ATM)
  Service policies
  Link efficiency mechanisms
AutoQoS lends itself to tuning of all generated parameters & configurations

## Slide 18: AutoQoS: Switch Platforms
6500
4500
3750
3560
3550
2970
2950EI
Cisco Catalyst 6500, 4500, 3550, 3560, 2970 and 2950(EI) Switches
User can meet the voice QoS requirements without extensive knowledge about:
  Trust boundary
  CoS to DSCP mappings
  Weighted Round Robin (WRR) & Priority Queue (PQ) Scheduling parameters
Generated parameters and configurations are user tunable

## Slide 19: AutoQoS: Switch Platforms (Cont.)
Single command at the interface level configures interface and global QoS
  Support for Cisco IP Phone & Cisco Soft Phone
  Support for Cisco Soft Phone currently exists only on the Cat6500
  Trust Boundary is disabled when IP Phone is moved / relocated
  Buffer Allocation & Egress Queuing dependent on interface type (GE/FE)
Supported on Static, dynamic-access, voice VLAN access, and trunk ports
CDP must be enabled for AutoQoS to function properly

## Slide 20: Configuring AutoQoS: Prerequisites for Using AutoQoS
Cisco Express Forwarding (CEF) must be enabled at the interface or ATM PVC
This feature cannot be configured if a QoS policy (service policy) is attached to the interface
An interface is classified as low-speed if its bandwidth is less than or equal to 768 kbps. It is classified as high-speed if its bandwidth is greater than 768 kbps
  The correct bandwidth should be configured on all interfaces or sub-interfaces using the bandwidth command
  If the interface or sub-interface has a link speed of 768 kbps or lower, an IP address must be configured using the ip address command

## Slide 21: Configuring AutoQoS: Routers
auto qos voip [trust] [fr-atm]
router(config-if)# or router(config-fr-dlci)#
Configures the AutoQoS VoIP feature
Untrusted mode by default
trust: Indicates that the differentiated services code point (DSCP) markings of a packet are trusted (relied on) for classification of the voice traffic
fr-atm: For low-speed Frame Relay DLCIs interconnected with ATM PVCs in the same network, the fr-atm keyword must be explicitly configured in the auto qos voip command to configure the AutoQoS VoIP feature properly

## Slide 22: Configuring AutoQoS: Cisco Catalyst 6500 Switch
Console>(enable)set qos autoqos
QoS is enabled
.........
All ingress and egress QoS scheduling parameters configured on all ports.CoS to DSCP, DSCP to COS, IP Precedence to DSCP and policed dscp maps configured. Global QoS configured, port specific autoqos recommended:
set port qos <mod/port> autoqos trust <cos|dscp>
set port qos <mod/port> autoqos voip <ciscoipphone|ciscosoftphone>
set qos autoqos
Console> (enable)
Global configuration command
All the global QoS settings are applied to all ports in the switch
Prompt displays showing the CLI for the port-based automatic QoS commands currently supported

## Slide 23: Configuring AutoQoS: Cisco Catalyst 6500 Switch (Cont.)
set port qos autoqos <mod/port> trust [cos|dscp]
Console> (enable)
trust dscp and trust cos are automatic QoS keywords used for ports requiring a "trust all" type of solution.
trust dscp should be used only on ports that connect to other switches or known servers as the port will be trusting all inbound traffic marking Layer 3 (DSCP)
trust cos should only be used on ports connecting other switches or known servers as the port trusts all inbound traffic marking in Layer 2 (CoS).
The trusted boundary feature is disabled and no QoS policing is configured on these types of ports

## Slide 24: Configuring AutoQoS: Cisco Catalyst 6500 Switch (Cont.)
set port qos autoqos <mod/port> voip [ciscosoftphone | ciscoipphone]
Console> (enable)
ciscosoftphone
The trusted boundary feature must be disabled for Cisco SoftPhone ports
QoS settings must be configured to trust the Layer 3 markings of the traffic that enters the port
Only available on Catalyst 6500
ciscoipphone
The port is set up to trust-cos as well as to enable the trusted boundary feature
Combined with the global automatic QoS command, all settings are configured on the switch to properly handle the signaling and voice bearer and PC data entering and leaving the port
CDP must be enabled for the ciscoipphone QoS configuration

## Slide 25: Configuring AutoQoS: Catalyst 2950EI, 3550 Switches
auto qos voip trust
Switch(config-if)#
The uplink interface is connected to a trusted switch or router, and the VoIP classification in the ingress packet is trusted
auto qos voip cisco-phone
Switch(config-if)#
Automatically enables the trusted boundary feature, which uses the CDP to detect the presence or absence of a Cisco IP Phone
If the interface is connected to a Cisco IP Phone, the QoS labels of incoming packets are trusted only when the IP phone is detected

## Slide 26: Monitoring AutoQoS: Routers
show auto qos [interface interface type]
router>
router>show auto qos interface Serial6/0
Serial6/0 –
!
interface Serial6/0
service-policy output AutoQoS-Policy-UnTrust
Displays the interface configurations, policy maps, class maps, and ACLs created on the basis of automatically generated configurations

## Slide 27: Monitoring AutoQoS: Routers (Cont.)
router>show policy-map interface FastEthernet0/0.1
FastEthernet0/0.1
Service-policy output: voice_traffic
Class-map: dscp46 (match-any)
0 packets, 0 bytes
5 minute offered rate 0 bps, drop rate 0 bps
Match: ip dscp 46
0 packets, 0 bytes
5 minute rate 0 bps
Traffic Shaping
Target Byte Sustain Excess Interval Increment Adapt
Rate Limit bits/int bits/int (ms) (bytes) Active
2500 10000 10000 333 1250 -
……rest deleted
show policy-map interface [interface type]
router>
Displays the packet statistics of all classes that are configured for all service policies either on the specified interface or subinterface

## Slide 28: Monitoring AutoQoS: Switches
show auto qos [interface interface-id]
Switch#
Switch#show auto qos
Initial configuration applied by AutoQoS:
wrr-queue bandwidth 20 1 80 0
no wrr-queue cos-map
wrr-queue cos 1 0 1 2 4
wrr-queue cos 3 3 6 7
wrr-queue cos 4 5
mls qos map cos-dscp 0 8 16 26 32 46 48 56
!
interface FastEthernet0/3
mls qos trust device cisco-phone
mls qos trust cos
Displays the auto-QoS configuration that was initially applied
Does not display any user changes to the configuration that might be in effect

## Slide 29: Monitoring AutoQoS: Switches (Cont.)
Switch#show mls qos interface gigabitethernet0/1 statistics
Ingress
dscp: incoming no_change classified policed dropped (in bytes)
1 : 0 0 0 0 0
Others: 203216935 24234242 178982693 0 0
Egress
dscp: incoming no_change classified policed dropped (in bytes)
1 : 0 n/a n/a 0 0
WRED drop counts:
qid thresh1 thresh2 FreeQ
1 : 0 0 1024
2 : 0 0 1024
………rest deleted
show mls qos interface [interface-id | vlan vlan-id] [buffers | policers | queueing | statistics] [ | {begin | exclude | include} expression]
Switch#
Displays QoS information at the interface level

## Slide 30: Monitoring AutoQoS: Switches (Cont.)
show mls qos maps [cos-dscp | dscp-cos | dscp-mutation dscp-mutation-name | dscp-switch-priority | ip-prec-dscp | policed-dscp] [ | {begin | exclude | include} expression
Switch#
Switch#show mls qos maps dscp-cos
Dscp-cos map:
dscp: 0 8 10 16 18 24 26 32 34 40 46 48 56
-----------------------------------------------
cos: 0 1 1 2 2 3 7 4 4 5 5 7 7
Maps are used to generate an internal Differentiated Services Code Point (DSCP) value, which represents the priority of the traffic

## Slide 31: Automation with Cisco AutoQoS: DiffServ Functions Automated

## Slide 32: Comparing Voice Quality Measurement Standards
Notes: Thanks for joining us today to attend the Cisco Brand and Corporate Identity Workshop.
In the first half of the workshop I am going to cover Brand Matters and talk in detail about the Cisco brand, and in the second half my colleague Gary McCavvit is going to take you through our updated visual identity system.
At the end of the workshop we’re going to leave some time for a fun quiz as well as some Q&A.

## Slide 33: Factors Affecting Audio Clarity
Fidelity (transmission bandwidth versus original)
Echo
Delay
Delay variation (jitter)

## Slide 34: VoIP Challenges
Notes: Thanks for joining us today to attend the Cisco Brand and Corporate Identity Workshop.
In the first half of the workshop I am going to cover Brand Matters and talk in detail about the Cisco brand, and in the second half my colleague Gary McCavvit is going to take you through our updated visual identity system.
At the end of the workshop we’re going to leave some time for a fun quiz as well as some Q&A.

## Slide 35: IP Networking Overview
IP networks assume delay, delay variation, and packet ordering problems.

## Slide 36: Jitter in IP Networks

## Slide 37: Sources of Delay

## Slide 38: Acceptable Delay: G.114

## Slide 39: QoS and Good Design
Notes: Thanks for joining us today to attend the Cisco Brand and Corporate Identity Workshop.
In the first half of the workshop I am going to cover Brand Matters and talk in detail about the Cisco brand, and in the second half my colleague Gary McCavvit is going to take you through our updated visual identity system.
At the end of the workshop we’re going to leave some time for a fun quiz as well as some Q&A.

## Slide 40: What Is QoS and Why Is It Needed?
Delay
Delay variation (jitter)
Packet loss

## Slide 41: Objectives of QoS
QoS has the following objectives:
Supporting dedicated bandwidth
Improving loss characteristics
Avoiding and managing network congestion
Shaping network traffic
Setting traffic priorities across the network

## Slide 42: Applying QoS

## Slide 43: Jitter
Notes: Thanks for joining us today to attend the Cisco Brand and Corporate Identity Workshop.
In the first half of the workshop I am going to cover Brand Matters and talk in detail about the Cisco brand, and in the second half my colleague Gary McCavvit is going to take you through our updated visual identity system.
At the end of the workshop we’re going to leave some time for a fun quiz as well as some Q&A.

## Slide 44: What Is Jitter?

## Slide 45: Playout Delay Buffer

## Slide 46: Dropped Packets

## Slide 47: Jitter Buffer Operation

## Slide 48: Adjusting Playout Delay
Choppy or jerky audio
High network delay
Jitter at the transmission end
Playout delay parameters must be adjusted in the following conditions:
Notes: Lesson Aim
  <Enter lesson aim here.>

## Slide 49: Symptoms of Jitter
Router# show call active voice
<output omitted>
VOIP:
ConnectionId[0xECDE2E7B 0xF46A003F 0x0 0x47070A4]
IncomingConnectionId[0xECDE2E7B 0xF46A003F 0x0 0x47070A4]
RemoteIPAddress=192.168.100.101
RemoteUDPPort=18834
RoundTripDelay=11 ms
SelectedQoS=best-effort
tx_DtmfRelay=inband-voice
FastConnect=TRUE
Separate H245 Connection=FALSE
H245 Tunneling=FALSE
Notes: Lesson Aim
  <Enter lesson aim here.>

## Slide 50: Symptoms of Jitter (Cont.)
SessionProtocol=cisco
SessionTarget=
OnTimeRvPlayout=417000
GapFillWithSilence=850 ms
GapFillWithPrediction=2590 ms
GapFillWithInterpolation=0 ms
GapFillWithRedundancy=0 ms
HiWaterPlayoutDelay=70 ms
LoWaterPlayoutDelay=29 ms
ReceiveDelay=39 ms
LostPackets=0
EarlyPackets=0
LatePackets=86
Notes: Lesson Aim
  <Enter lesson aim here.>

## Slide 51: Average Jitter Statistics
# show call active voice
<output omitted>
.
.
.
VOIP:
ConnectionId[0xECDE2E7B 0xF46A003F 0x0 0x47070A4]
IncomingConnectionId[0xECDE2E7B 0xF46A003F 0x0 0x47070A4]
RemoteIPAddress=192.168.100.101
RemoteUDPPort=18834
RoundTripDelay=26 ms
SelectedQoS=best-effort
tx_DtmfRelay=inband-voice
FastConnect=TRUE
Separate H245 Connection=FALSE
H245 Tunneling=FALSE
Notes: Lesson Aim
  <Enter lesson aim here.>

## Slide 52: Average Jitter Statistics (Cont.)
SessionProtocol=cisco
SessionTarget=
OnTimeRvPlayout=482350
GapFillWithSilence=1040 ms <------------ Increased
GapFillWithPrediction=3160 ms <------------ Increased
GapFillWithInterpolation=0 ms
GapFillWithRedundancy=0 ms
HiWaterPlayoutDelay=70 ms
LoWaterPlayoutDelay=29 ms
ReceiveDelay=43 ms <------------ Increased
LostPackets=0
EarlyPackets=0
LatePackets=105 <------------ Increased
Notes: Lesson Aim
  <Enter lesson aim here.>

## Slide 53: Dynamic Mode

## Slide 54: Static Mode

## Slide 55: Delay
Notes: Thanks for joining us today to attend the Cisco Brand and Corporate Identity Workshop.
In the first half of the workshop I am going to cover Brand Matters and talk in detail about the Cisco brand, and in the second half my colleague Gary McCavvit is going to take you through our updated visual identity system.
At the end of the workshop we’re going to leave some time for a fun quiz as well as some Q&A.

## Slide 56: Delay Budget

## Slide 57: Acceptable Delay: G.114

## Slide 58: Sources of Delay
Coder delay
Packetization delay
Queuing delay
Serialization delay
Network delay
Dejitter buffer delay

## Slide 59: Coder Delay

## Slide 60: Serialization Delay

## Slide 61: Fragmentation Using FRF.12

## Slide 62: Verifying End-to-End Delay

## Slide 63: Apply QoS in the Campus
Notes: Thanks for joining us today to attend the Cisco Brand and Corporate Identity Workshop.
In the first half of the workshop I am going to cover Brand Matters and talk in detail about the Cisco brand, and in the second half my colleague Gary McCavvit is going to take you through our updated visual identity system.
At the end of the workshop we’re going to leave some time for a fun quiz as well as some Q&A.

## Slide 64: Need for QoS in the Campus

## Slide 65: Marking Control and Management Traffic

## Slide 66: Configuring a Voice VLAN
Router# configure terminal
Router(config)# interface fastethernet 5/1
Router(config-if)# switchport voice vlan 101
Router(config-if)# exit

## Slide 67: Verifying the Configuration
Router# show interfaces fastethernet 5/1 switchport
Name: Fa5/1
Switchport: Enabled
Administrative Mode: access
Operational Mode: access
Administrative Trunking Encapsulation: dot1q
Operational Trunking Encapsulation: dot1q
Negotiation of Trunking: off
Access Mode VLAN: 100
Voice VLAN: 101
Trunking Native Mode VLAN: 1 (default)
Administrative private-vlan host-association: none
Administrative private-vlan mapping: 900 ((Inactive)) 901 ((Inactive))
Operational private-vlan: none
Trunking VLANs Enabled: ALL
Pruning VLANs Enabled: 2-1001
Capture Mode Disabled
Capture VLANs Allowed: ALL

## Slide 68: QoS Tools in the WAN
Notes: Thanks for joining us today to attend the Cisco Brand and Corporate Identity Workshop.
In the first half of the workshop I am going to cover Brand Matters and talk in detail about the Cisco brand, and in the second half my colleague Gary McCavvit is going to take you through our updated visual identity system.
At the end of the workshop we’re going to leave some time for a fun quiz as well as some Q&A.

## Slide 69: Need for QoS in the WAN
Voice must compete with data.
Voice is real-time and must be sent first.
Overhead should be minimized.
Large data packets delay smaller voice packets.
WAN delay variation must be minimized.
WANs should not be oversubscribed.

## Slide 70: Generic QoS Tools
Bandwidth provisioning
Prioritization
Link efficiency
LFI
Traffic shaping
CAC
QoS measures that are necessary in the WAN include the following:

## Slide 71: Bandwidth Provisioning

## Slide 72: Optimized Queuing

## Slide 73: Link Efficiency: CRTP

## Slide 74: IP Precedence vs. DSCP

## Slide 75: AF and DSCP Values

## Slide 76: Link Fragmentation and Interleaving

## Slide 77: Call Admission Control

## Slide 78: Configuring QoS in the WAN
Notes: Thanks for joining us today to attend the Cisco Brand and Corporate Identity Workshop.
In the first half of the workshop I am going to cover Brand Matters and talk in detail about the Cisco brand, and in the second half my colleague Gary McCavvit is going to take you through our updated visual identity system.
At the end of the workshop we’re going to leave some time for a fun quiz as well as some Q&A.

## Slide 79: Configuring AutoQoS

## Slide 80: Configuring AutoQoS (Cont.)

## Slide 81: Configuring CAC
Notes: Thanks for joining us today to attend the Cisco Brand and Corporate Identity Workshop.
In the first half of the workshop I am going to cover Brand Matters and talk in detail about the Cisco brand, and in the second half my colleague Gary McCavvit is going to take you through our updated visual identity system.
At the end of the workshop we’re going to leave some time for a fun quiz as well as some Q&A.

## Slide 82: Need for Call Admission Control

## Slide 83: Call Control Approach to CAC

## Slide 84: RSVP

## Slide 85: Understanding CAC Tools
H.323 CAC
SIP CAC
MGCP CAC
CallManager CAC

## Slide 86: H.323 CAC
call threshold {global trigger-name | interface interface-name interface-number int-calls} low value high value [busyout | treatment]
call spike call-number [steps number-of-steps size milliseconds]
call treatment {on | action action [value] | cause-code cause-code | isdn-reject value}

## Slide 87: Voice Bandwidth Engineering
Notes: Thanks for joining us today to attend the Cisco Brand and Corporate Identity Workshop.
In the first half of the workshop I am going to cover Brand Matters and talk in detail about the Cisco brand, and in the second half my colleague Gary McCavvit is going to take you through our updated visual identity system.
At the end of the workshop we’re going to leave some time for a fun quiz as well as some Q&A.

## Slide 88: Erlangs
The amount of traffic a trunk can handle in one hour.
Equals
  60 call minutes
  3600 call seconds
  36 centum call seconds (CCS)