## Slide 1: Distance Vector Routing Protocols
Routing Protocols and Concepts – Chapter 4

## Slide 2: Objectives
Identify the characteristics of distance vector routing protocols.
Describe the network discovery process of distance vector routing protocols using Routing Information Protocol (RIP).
Describe the processes to maintain accurate routing tables used by distance vector routing protocols.
Identify the conditions leading to a routing loop and explain the implications for router performance.
Recognize that distance vector routing protocols are in use today

## Slide 3: Distance Vector Routing Protocols
Examples of Distance Vector routing protocols:
    Routing Information Protocol (RIP)
    Interior Gateway Routing Protocol (IGRP)
    Enhanced Interior Gateway Routing Protocol (EIGRP)

## Slide 4: Distance Vector Routing Protocols
Distance Vector Technology
  The Meaning of Distance Vector:
    A router using distance vector routing protocols knows 2 things:
        Distance to final destination
        Vector, or direction, traffic should be directed

## Slide 5: Distance Vector Routing Protocols
Characteristics of Distance Vector routing protocols:
  Periodic updates
  Neighbors
  Broadcast updates
  Entire routing table is included with routing update

## Slide 6: Distance Vector Routing Protocols
Routing Protocol Algorithm:
-Defined as a procedure for accomplishing a certain task

## Slide 7: Distance Vector Routing Protocols
Routing Protocol Characteristics
  Criteria used to compare routing protocols includes
    -Time to convergence
    -Scalability
    -Resource usage
    -Implementation & maintenance

## Slide 8: Distance Vector Routing Protocols

## Slide 9: Network Discovery
Router initial start up (Cold Starts)
  -Initial network discovery
    Directly connected networks are initially placed in routing table

## Slide 10: Network Discovery
Initial Exchange of Routing Information
  If a routing protocol is configured then
-Routers will exchange routing information
Routing updates received from other routers
-Router checks update for new information
      If there is new information:
-Metric is updated
-New information is
stored in routing table

## Slide 11: Network Discovery
Exchange of Routing Information
  Router convergence is reached when
-All routing tables in the network contain the same network information
  Routers continue to exchange routing information
-If no new information is found then Convergence is reached

## Slide 12: Network Discovery
Convergence must be reached before a network is considered completely operable
Speed of achieving convergence consists of 2 interdependent categories
-Speed of broadcasting routing information
-Speed of calculating routes

## Slide 13: Routing Table Maintenance
Periodic Updates: RIPv1 & RIPv2
These are time intervals in which a router sends out its entire routing table.

## Slide 14: Routing Table Maintenance
RIP uses 4 timers
  -Update timer
  -Invalid timer
  -Holddown timer
  -Flush timer

## Slide 15: Routing Table Maintenance
Bounded Updates: EIGRP
EIRPG routing updates are
-Partial updates
-Triggered by topology changes
-Bounded
-Non periodic

## Slide 16: Routing Table Maintenance
Triggered Updates
  Conditions in which triggered updates are sent
-Interface changes state
-Route becomes unreachable
-Route is placed in routing table

## Slide 17: Routing Table Maintenance
Random Jitter
  Synchronized updates
    A condition where multiple routers on multi access LAN segments transmit routing updates at the same time.
    Problems with synchronized updates
      -Bandwidth consumption
      -Packet collisions
    Solution to problems with
    synchronized updates
- Used of random variable
called RIP_JITTER

## Slide 18: Routing Loops
Routing loops are
A condition in which a packet is continuously transmitted within a series of routers without ever reaching its destination.

## Slide 19: Routing Loops
Routing loops may be caused by:
-Incorrectly configured static routes
-Incorrectly configured route redistribution
-Slow convergence
-Incorrectly configured discard routes
Routing loops can create the following issues
-Excess use of bandwidth
-CPU resources may be strained
-Network convergence is degraded
-Routing updates may be lost or not processed in a timely manner

## Slide 20: Routing Loops
Count to Infinity
This is a routing loop whereby packets bounce infinitely around a network.

## Slide 21: Routing Loops
Setting a maximum
Distance Vector routing protocols set a specified metric value to indicate infinity
Once a router “counts to infinity” it marks the route as unreachable

## Slide 22: Routing Loops
Preventing loops with holddown timers
  -Holddown timers allow a router to not accept any changes to a route for a specified period of time.
  -Point of using holddown timers
    Allows routing updates to propagate through network with the most current information.

## Slide 23: Routing Loops
The Split Horizon Rule is used to prevent routing loops
Split Horizon rule:
A router should not advertise a network through the interface from which the update came.

## Slide 24: Routing Loops
Split horizon with poison reverse
The rule states that once a router learns of an unreachable route through an interface, advertise it as unreachable back through the same interface

## Slide 25: Routing Loops
IP & TTL
  Purpose of the TTL field
The TTL field is found in an IP header and is used to prevent packets from endlessly traveling on a network
How the TTL field works
-TTL field contains a numeric value
The numeric value is decreased by one by every router on the route to the destination.
If numeric value reaches 0 then Packet is discarded.

## Slide 26: Routing Protocols Today
Factors used to determine whether to use RIP or EIGRP include
-Network size
-Compatibility between models of routers
-Administrative knowledge

## Slide 27: Routing Protocols Today
RIP
  Features of RIP:
-Supports split horizon & split horizon with poison reverse
-Capable of load balancing
-Easy to configure
-Works in a multi vendor router environment

## Slide 28: Routing Protocols Today
EIGRP
  Features of EIGRP:
-Triggered updates
-EIGRP hello protocol used to establish neighbor adjacencies
-Supports VLSM & route summarization
-Use of topology table to maintain all routes
-Classless distance vector routing protocol
-Cisco proprietary protocol

## Slide 29: Summary
Characteristics of Distance Vector routing protocols
  Periodic updates
  RIP routing updates include the entire routing table
  Neighbors are defined as routers that share a link and are configured to use the same protocol
The network discovery process for D.V. routing protocol
  Directly connected routes are placed in routing table 1st
  If a routing protocol is configured then
    Routers will exchange routing information
  Convergence is reached when all network routers have the
  same network information

## Slide 30: Summary
D.V. routing protocols maintains routing tables by
  RIP sending out periodic updates
  RIP using 4 different timers to ensure information is accurate and convergence is achieved in a timely manner
  EIGRP sending out triggered updates
D.V. routing protocols may be prone to routing loops
  routing loops are a condition in which packets continuously traverse a network
  Mechanisms used to minimize routing loops include defining maximum hop count, holddown timers, split horizon, route poisoning and triggered updates

## Slide 31: Summary
Conditions that can lead to routing loops include
  Incorrectly configured static routes
  Incorrectly configured route redistribution
  Slow convergence
  Incorrectly configured discard routes
How routing loops can impact network performance includes:
  Excess use of bandwidth
  CPU resources may be strained
  Network convergence is degraded
  Routing updates may be lost or not processed

## Slide 32: Summary
Routing Information Protocol (RIP)
  A distance vector protocol that has 2 versions
  RIPv1 – a classful routing protocol
  RIPv2 - a classless routing protocol
Enhanced Interior Gateway Routing Protocol (EIGRP)
  A distance vector routing protocols that has some features of link state routing protocols
  A Cisco proprietary routing protocol