## Slide 1: EIGRP
Routing Protocols and Concepts – Chapter 9

## Slide 2: Objectives
Describe the background and history of Enhanced Interior Gateway Routing Protocol (EIGRP).
Examine the basic EIGRP configuration commands and identify their purposes.
Calculate the composite metric used by EIGRP.
Describe the concepts and operation of DUAL.
Describe the uses of additional configuration commands in EIGRP.

## Slide 3: Introduction

## Slide 4: EIGRP
Roots of EIGRP: IGRP
  -Developed in 1985 to overcome RIPv1’s limited hop count
  -Distance vector routing protocol
  -Metrics used by IGRP
    bandwidth (used by default)
    Delay (used by default)
    reliability
    load
  -Discontinued support starting with IOS 12.2(13)T & 12.2(R1s4)S

## Slide 5: EIGRP
EIGRP Message Format
EIGRP Header
  Data link frame header - contains source and destination MAC address
  IP packet header - contains source & destination IP address
  EIGRP packet header - contains AS number
  Type/Length/Field - data portion of EIGRP message

## Slide 6: EIGRP
EIGRP packet header contains
  Opcode field
  Autonomous System number
EIGRP Parameters contains
  Weights
  Hold time

## Slide 7: EIGRP
TLV: IP internal contains
  Metric field
  Subnet mask field
  Destination field
TLV: IP external contains
  Fields used when external
  routes are imported into
  EIGRP routing process

## Slide 8: EIGRP
Protocol Dependent Modules (PDM)
EIGRP uses PDM to route several different protocols i.e. IP, IPX & AppleTalk
PDMs are responsible for the specific routing task for each network layer protocol

## Slide 9: EIGRP
Reliable Transport Protocol (RTP)
Purpose of RTP
  Used by EIGRP to transmit and receive EIGRP packets
Characteristics of RTP
  Involves both reliable & unreliable delivery of EIGRP packet
    Reliable delivery requires acknowledgment from destination
    Unreliable delivery does not require an acknowledgement from destination
  Packets can be sent
    Unicast
    Multicast
      Using address 224.0.0.10

## Slide 10: EIGRP
EIGRP’s 5 Packet Types
Hello packets
  Used to discover & form adjacencies with neighbors

## Slide 11: EIGRP
Update packets
  Used to propagate routing information
Acknowledgement packets
  Used to acknowledge receipt of update, query & reply packets

## Slide 12: EIGRP
Query & Reply packets
  Used by DUAL for searching for networks
  Query packets
    -Can use
      Unicast
      Multicast
  Reply packet
    -Use only
      unicast

## Slide 13: EIGRP
Purpose of Hello Protocol
  To discover & establish adjacencies with neighbor routers
Characteristics of hello protocol
  Time interval for sending hello packet
    Most networks it is every 5 seconds
    Multipoint non broadcast multi-access networks
      Unicast every 60 seconds
-Holdtime
    This is the maximum time router should wait before declaring a neighbor down
    Default holdtime
      3 times hello interval

## Slide 14: EIGRP
EIGRP Bounded Updates
EIGRP only sends update when there is a change in route status
Partial update
  A partial update includes only the route information that has changed – the whole routing table is NOT sent
Bounded update
  When a route changes, only those devices that are impacted will be notified of the change
EIGRP’s use of partial bounded updates minimizes use of bandwidth

## Slide 15: EIGRP
Diffusing Update Algorithm (DUAL)
  Purpose
    EIGRP’s primary method for preventing routing loops
  Advantage of using DUAL
    Provides for fast convergence time by keeping a list of loop-free backup routes

## Slide 16: EIGRP
Administrative Distance (AD)
  Defined as the trustworthiness of the source route
EIGRP default administrative distances
  Summary routes = 5
  Internal routes = 90
  Imported routes = 170

## Slide 17: EIGRP
Authentication
EIGRP can
  Encrypt routing information
  Authenticate routing information

## Slide 18: EIGRP
Network Topology
Topology used is the same as previous chapters with the addition of an ISP router

## Slide 19: EIGRP
EIGRP will automatically summarize routes at classful boundaries

## Slide 20: Basic EIGRP Configuration
Autonomous System (AS) & Process IDs
  This is a collection of networks under the control of a single authority (reference RFC 1930)
  AS Numbers are assigned by IANA
  Entities needing AS numbers
    ISP
    Internet Backbone prodiers
    Institutions connecting to other institutions using AS numbers

## Slide 21: Basic EIGRP Configuration
EIGRP autonomous system number actually functions as a process ID
Process ID represents an instance of the routing protocol running on a router
Example
Router(config)#router
eigrp autonomous-system

## Slide 22: Basic EIGRP Configuration
The router eigrp command
The global command that enables eigrp is
  router eigrp autonomous-system
  -All routers in the EIGRP routing domain must use the same process ID number (autonomous-system number)

## Slide 23: Basic EIGRP Configuration
The Network Command
Functions of the network command
  Enables interfaces to transmit & receive EIGRP updates
  Includes network or subnet in EIGRP updates
Example
  Router(config-router)#network network-address

## Slide 24: Basic EIGRP Configuration
The network Command with a Wildcard Mask
  -This option is used when you want to configure EIGRP to advertise specific subnets
  -Example
  Router(config-router)#network network-address [wildcard-mask]

## Slide 25: Basic EIGRP Configuration
Verifying EIGRP
EIGRP routers must establish adjacencies with their neighbors before any updates can be sent or received
Command used to view neighbor table and verify that EIGRP has established adjacencies with neighbors is
  show ip eigrp neighbors

## Slide 26: EIGRP
The show ip protocols command is also used to verify that EIGRP is enabled

## Slide 27: Basic EIGRP Configuration
Examining the Routing Table
The show ip route command is also used to verify EIGRP
EIGRP routes are denoted in a routing table by the letter “D”
By default , EIGRP automatically summarizes routes at major network boundary

## Slide 28: Basic EIGRP Configuration
Introducing the Null0 Summary Route
  Null0 is not a physical interface
  In the routing table summary routes are sourced from Null0
    Reason: routes are used for advertisement purposes
  EIGRP will automatically include a null0 summary route as child route when 2 conditions are met
    At least one subnet is learned via EIGRP
    Automatic summarization is enabled

## Slide 29: Basic EIGRP Configuration
R3’s routing table shows that the 172.16.0.0/16 network is automatically summarized by R1 & R3

## Slide 30: EIGRP Metric Calculation
EIGRP Composite Metric & the K Values
EIGRP uses the following values in its composite metric
  -Bandwidth, delay, reliability, and load
The composite metric used by EIGRP
  formula used has values K1 K5
      K1 & K3 = 1
      all other K values = 0

## Slide 31: EIGRP Metric Calculation
Use the sh ip protocols command to verify the K values

## Slide 32: EIGRP Metric Calculation
EIGRP Metrics
Use the show interfaces command to view metrics
EIGRP Metrics
  Bandwidth – EIGRP uses a static bandwidth to calculate metric
  Most serial interfaces use a default bandwidth value of 1.544Mbos (T1)

## Slide 33: EIGRP Metric Calculation
EIGRP Metrics
Delay is the defined as the measure of time it takes for a packet to traverse a route
  -it is a static value based on link type to which interface is connected

## Slide 34: EIGRP Metric Calculation
Reliability (not a default EIGRP metric)
  -A measure of the likelihood that a link will fail
  -Measure dynamically & expressed as a fraction of 255
  the higher the fraction the better the reliability
Load (not a default EIGRP metric)
  A number that reflects how much traffic is using a link
  Number is determined dynamically and is expressed as a fraction of 255
    The lower the fraction the less the load on the link

## Slide 35: EIGRP Metric Calculation
Using the Bandwidth Command
Modifying the interface bandwidth
  -Use the bandwidth command
  -Example
  Router(config-if)#bandwidth kilobits
Verifying bandwidth
  Use the show interface command
Note – bandwidth command
does not change the
link’s physical
bandwidth

## Slide 36: EIGRP Metric Calculation
The EIGRP metric can be determined by examining the
bandwidth delay

## Slide 37: EIGRP Metric Calculation
EIGRP uses the lowest bandwidth (BW)in its metric calculation
Calculated BW = reference BW / lowest BW(kbps)
Delay – EIGRP uses the cumulative sum of all outgoing interfaces
  Calculated Delay = the sum of outgoing interface delays
EIGRP Metric = calculated BW + calculated delay

## Slide 38: EIGRP Metric Calculation

## Slide 39: DUAL Concepts
The Diffusing Update Algorithm (DUAL) is used to prevent looping

## Slide 40: DUAL Concepts
Successor
  The best least cost route to a destination found in the routing table
Feasible distance
  The lowest calculated metric along a path to a destination network

## Slide 41: DUAL Concepts
Feasible Successors, Feasibility Condition & Reported Distance
Feasible Successor
  -This is a loop free backup route to same
  destination as successor route

## Slide 42: DUAL Concepts
Reported distance (RD)
  -The metric that a router reports to a neighbor about its own cost to that network
Feasible Successors, Feasibility Condition & Reported Distance

## Slide 43: DUAL Concepts
Feasibility Condition (FC)
  -Met when a neighbor’s RD is less than the local router’s FD to the same destination network

## Slide 44: DUAL Concepts
Topology Table: Successor & Feasible Successor
EIGRP Topology table
  Viewed using the show ip eigrp topology command
    Contents of table include:
      all successor routes
      all feasible successor routes

## Slide 45: DUAL Concepts
EIGRP Topology Table dissected

## Slide 46: DUAL Concepts
Topology Table: No Feasible Successor
A feasible successor may not be present because the feasibility condition may not be met
  -In other words, the reported distance of the neighbor is greater than or equal to the current feasible distance

## Slide 47: DUAL Concepts
Finite Sate Machine (FSM)
  An abstract machine that defines a set of possible states something can go through, what event causes those states and what events result form those states
  FSMs are used to describe how a device, computer program, or routing algorithm will react to a set of input events

## Slide 48: DUAL Concepts
DUAL FSM
  Selects a best loop-free path to a destination
  Selects alternate routes by using information in EIGRP tables

## Slide 49: DUAL Concepts
Finite State Machines (FSM)
To examine output from EIGRP’s finite state machine us the debug eigrp fsm command

## Slide 50: More EIGRP Configurations
The Null0 Summary Route
By default, EIGRP uses the Null0 interface to discard any packets that match the parent route but do not match any of the child routes
EIGRP automatically includes a null0 summary route as a child route whenever both of the following conditions exist
  One or subnets exists that was learned via EIGRP
  Automatic summarization is enabled

## Slide 51: More EIGRP Configurations
The Null0 Summary Route

## Slide 52: More EIGRP Configurations
Disabling Automatic Summarization
The auto-summary command permits EIGRP to automatically summarize at major network boundaries
The no auto-summary command is used to disable automatic summarization
  This causes all EIGRP neighbors to send updates that will not be automatically summarized
    this will cause changes to appear in both
        -routing tables
        -topology tables

## Slide 53: More EIGRP Configurations
Manual Summarization
Manual summarization can include supernets
  Reason: EIGRP is a classless routing protocol & include subnet mask in update
Command used to configure manual summarization
  Router(config-if)#ip summary-address eigrp as-number network-address subnet-mask

## Slide 54: More EIGRP Configurations
Configuring a summary route in EIGRP

## Slide 55: More EIGRP Configurations
EIGRP Default Routes
“quad zero” static default route
  -Can be used with any currently supported routing protocol
  -Is usually configured on a router that is connected a network outside the EIGRP domain
EIGRP & the “Quad zero” static default route
  Requires the use of the redistribute static command to disseminate default route in EIGRP updates

## Slide 56: More EIGRP Configurations
Fine-Tuning EIGRP
EIGRP bandwidth utilization
  -By default, EIGRP uses only up to 50% of interface bandwidth for EIGRP information
  -The command to change the percentage of bandwidth used by EIGRP is
  Router(config-if)#ip bandwidth-percent eigrp as- number percent

## Slide 57: More EIGRP Configurations
Configuring Hello Intervals and Hold Times
  -Hello intervals and hold times are configurable on a per-interface basis
  -The command to configure hello interval is
  Router(config-if)#ip hello-interval eigrp as-number seconds
Changing the hello interval also requires changing the hold time to a value greater than or equal to the hello interval
  -The command to configure hold time value is
  Router(config-if)#ip hold-time eigrp as-number seconds

## Slide 58: Summary
Background & History
  EIGRP is a derivative of IGRP
    EIGRP is a Cisco proprietary distance vector routing protocol released in 1994
EIGRP terms and characteristics
  EIGPR uses RTP to transmit & receive EIGRP packets
  EIGRP has 5 packet type:
    Hello packets
    Update packets
    Acknowledgement packets
    Query packets
    Reply packets
  Supports VLSM & CIDR

## Slide 59: Summary
EIGRP terms and characteristics
  EIGRP uses a hello protocol
    Purpose of hello protocol is to discover & establish adjacencies
  EIGRP routing updates
    Aperiodic
    Partial and bounded
    Fast convergence

## Slide 60: Summary
EIGRP commands
  The following commands are used for EIGRP configuration
    RtrA(config)#router eigrp [autonomous-system #]
    RtrA(config-router)#network network-number
  The following commands can be used to verify EIGRP
    Show ip protocols
    Show ip eigrp neighbors
    Show ip route

## Slide 61: Summary
EIGRP metrics include
  Bandwidth (default)
  Delay (default)
  Reliability
  Load

## Slide 62: Summary
DUAL
  Purpose of DUAL
    To prevent routing loops
  Successor
    Primary route to a destination
  Feasible successor
    Backup route to a destination
  Feasible distance
    Lowest calculated metric to a destination
  Reported distance
    The distance towards a destination as advertised by an upstream neighbor

## Slide 63: Summary
Choosing the best route
  After router has received all updates from directly connected neighbors, it can calculate its DUAL
    1st metric is calculated for each route
    2nd route with lowest metric is designated successor & is placed in routing table
    3rd feasible successor is found
      Criteria for feasible successor: it must have lower reported distance to the destination than the installed route’s feasible distance
      Feasible routes are maintained in topology table

## Slide 64: Summary
Automatic summarization
  On by default
  Summarizes routes on classful boundary
  Summarization can be disabled using the following command
    RtrA(config-if)#no auto-summary