## Slide 1: RIP version 1
Routing Protocols and Concepts – Chapter 5

## Slide 2: Objectives
Describe the functions, characteristics, and operation of the RIPv1 protocol.
Configure a device for using RIPv1.
Verify proper RIPv1 operation.
Describe how RIPv1 performs automatic summarization.
Configure, verify, and troubleshoot default routes propagated in a routed network implementing RIPv1.
Use recommended techniques to solve problems related to RIPv1

## Slide 3: RIPv1
RIP Characteristics
-A classful, Distance Vector (DV) routing protocol
-Metric = hop count
-Routes with a hop count > 15 are unreachable
-Updates are broadcast every 30 seconds

## Slide 4: RIPv1
RIP Message Format
RIP header - divided into 3 fields
-Command field
-Version field
-Must be zero
Route Entry - composed of 3 fields
  -Address family identifier
  -IP address
  -Metric

## Slide 5: RIPv1
RIP Operation
  RIP uses 2 message types:
      Request message
-This is sent out on startup by each RIP enabled interface
-Requests all RIP enabled neighbors to send routing table
      Response message
-Message sent to requesting router containing routing table

## Slide 6: RIPv1
IP addresses initially divided into classes
-Class A
-Class B
-Class C
RIP is a classful routing protocol
-Does not send subnet masks in routing updates

## Slide 7: RIPv1
Administrative Distance
  RIP’s default administrative distance is 120

## Slide 8: Basic RIPv1 Configuration
A typical topology suitable for use by RIPv1 includes:
    -Three router set up
    -No PCs attached to LANs
-Use of 5 different IP subnets

## Slide 9: Basic RIPv1 Configuration
Router RIP Command
  To enable RIP enter:
  -Router rip at the global configuration prompt
  -Prompt will look like R1(config-router)#

## Slide 10: Basic RIPv1 Configuration
Specifying Networks
  Use the network command to:
  -Enable RIP on all interfaces that belong to this network
  -Advertise this network in RIP updates sent to other routers every 30 seconds

## Slide 11: Verification and Troubleshooting
Show ip Route
To verify and troubleshoot routing
-Use the following
commands:
-show ip route
-show ip protocols
-debug ip rip

## Slide 12: Verification and Troubleshooting
show ip protocols command
-Displays routing protocol configured on router

## Slide 13: Verification and Troubleshooting
Debug ip rip command
-Used to display RIP routing updates as they are happening

## Slide 14: Verification and Troubleshooting
Passive interface command
-Used to prevent a router from sending updates through an interface
-Example:
Router(config-router)#passive-interface interface-type interface-number

## Slide 15: Verification and Troubleshooting
Passive interfaces

## Slide 16: Automatic Summarization
Modified Topology
The original scenario has been modified such that:
Three classful networks are used:
172.30.0.0/16
192.168.4.0/24
192.168.5.0/24
The 172.30.0.0/16 network is subnetted into three subnets:
172.30.1.0/24
172.30.2.0/24
172.30.3.0/24
The following devices are part of the 172.30.0.0/16 classful network address:
All interfaces on R1
S0/0/0 and Fa0/0 on R2

## Slide 17: Automatic Summarization
Configuration Details
-To remove the RIP routing process use the following command
No router rip
-To check the configuration use the following command
Show run

## Slide 18: Automatic Summarization
Boundary Routers
  RIP automatically summarizes classful networks
  Boundary routers summarize RIP subnets from one major network to another.

## Slide 19: Automatic Summarization
Processing RIP Updates
2 rules govern RIPv1 updates:
-If a routing update and the interface it’s received on belong to the same network then
The subnet mask of the interface is applied to the network in the routing update
-If a routing update and the interface it’s received on belong to a different network then
The classful subnet mask of the network is applied to the network in the routing update.

## Slide 20: Automatic Summarization
Sending RIP Updates
  RIP uses automatic summarization to reduce the size of a routing table.

## Slide 21: Automatic Summarization
Advantages of automatic summarization:
-The size of routing updates is reduced
-Single routes are used to represent multiple routes which results in faster lookup in the routing table.

## Slide 22: Automatic Summarization
Disadvantage of Automatic Summarization:
-Does not support discontiguous networks

## Slide 23: Automatic Summarization
Discontiguous Topologies do not converge with RIPv1
A router will only advertise major network addresses out interfaces that do not belong to the advertised route.

## Slide 24: Default Route and RIPv1
Modified Topology: Scenario C
Default routes
  Packets that are not defined specifically in a routing table will go to the specified interface for the default route
  Example: Customer routers use default routes to connect to an ISP router.
  Command used to configure a default route is
  ip route 0.0.0.0 0.0.0.0 s0/0/1

## Slide 25: Default Route and RIPv1

## Slide 26: Default Route and RIPv1
Propagating the Default Route in RIPv1
Default-information originate command
  -This command is used to specify that the router is to originate default information, by propagating the static default route in RIP update.

## Slide 27: Summary
RIP characteristics include:
Classful, distance vector routing protocol
Metric is Hop Count
Does not support VLSM or discontiguous subnets
Updates every 30 seconds
Rip messages are encapsulated in a UDP segment with source and destination ports of 520

## Slide 28: Summary: Commands used by RIP
Command | Command’s purpose
Rtr(config)#router rip | Enables RIP routing process
Rtr(config-router)#network | Associates a network with a RIP routing process
Rtr#debug ip rip | used to view real time RIP routing updates
Rtr(config-router)#passive-interface fa0/0 | Prevent RIP updates from going out an interface
Rtr(config-router)#default-information originate | Used by RIP to propagate default routes
Rtr#show ip protocols | Used to display timers used by RIP