## Slide 1: The Routing Table: A Closer Look
Routing Protocols and Concepts – Chapter 8

## Slide 2: Objectives
Describe the various route types found in the routing table structure
Describe the routing table lookup process.
Describe routing behavior in routed networks.

## Slide 3: Introduction
Chapter Focus
-Structure of the routing table
-Lookup process of the routing table
-Classless and classful routing behaviors

## Slide 4: Routing Table Structure
Lab Topology
3 router setup
  -R1 and R2 share a common 172.16.0.0/16 network with 172.16.0.0/24 subnets.
  -R2 and R3 are connected by the 192.168.1.0/24 network.
  -R3 also has a 172.16.4.0/24 subnet, which is disconnected, or discontiguous, from the 172.16.0.0 network that R1 and R2 share.

## Slide 5: Routing Table Structure
Routing table entries come from the following sources
  -Directly connected networks
  -Static routes
  -Dynamic routing protocols

## Slide 6: Routing Table Structure
Level 1 Routes
As soon as the no shutdown command is issued the route is added to routing table

## Slide 7: Routing Table Structure
Cisco IP routing table is a hierarchical structure
-The reason for this is to speed up lookup process

## Slide 8: Routing Table Structure
Level 1 Routes
-Have a subnet mask equal to or less than the classful mask of the network address.
Level 1 route can function as
-Default route
-Supernet route
-Network route

## Slide 9: Routing Table Structure
Level 1 Routes
  -Ultimate Route
    Includes either:
-A next-hop address
OR
-An exit interface

## Slide 10: Routing Table Structure
Parent and Child Routes
-A parent route is a level 1 route
-A parent route does not contain any next-hop IP address or exit interface information

## Slide 11: Routing Table Structure
Automatic creation of parent routes
  -Occurs any time a subnet is added to the routing table
Child routes
-Child routes are level 2 routes
-Child routes are a subnet of a classful network address

## Slide 12: Routing Table Structure
Level 2 child routes contain route source & the network address of the route
Level 2 child routes are also considered ultimate routes
Reason: they contain the next hop address &/or exit interface

## Slide 13: Routing Table Structure
Both child routes have the same subnet mask
-This means the parent route maintains the /24 mask

## Slide 14: Routing Table Structure
Diagram illustrates 2 child networks belonging to the parent route 172.16.0.0 / 24

## Slide 15: Routing Table Structure
In classless networks, child routes do not have to share the same subnet mask

## Slide 16: Routing Table Structure
Network Type | Parent route’s Classful mask is Displayed | Term variably subnetted is seen in parent route in routing table | Includes the # of different masks of child routes | Subnet mask included with each child route entry
Class- ful | No | No | No | No
Class-less | Yes | Yes | Yes | Yes
Parent & Child Routes: Classless Networks

## Slide 17: Routing Table Structure
Parent & Child Routes: Classless Networks

## Slide 18: Routing Table Lookup Process
The Route Lookup Process
    Examine level 1 routes
      -If best match a level 1 ultimate route and is not a parent route this route is used to forward packet
    Router examines level 2 (child) routes
      -If there is a match with level 2 child route then
        that subnet is used to forward packet
      -If no match then
      determine routing behavior type
    Router determines classful or classless routing behavior
      -If classful then
        packet is dropped
      -If classless then router searches level one supernet and default routes
      -If there exists a level 1 supernet or default route match then Packet is forwarded. If not packet is dropped

## Slide 19: Routing Table Lookup Process
Longest Match: Level 1 Network Routes
  Best match is also known as the longest match
  The best match is the one that has the most number of left most bits matching between the destination IP address and the route in the routing table.

## Slide 20: Routing Table Lookup Process
Finding the subnet mask used to determine the longest match
Scenario:
  PC1 pings 192.168.1.2
  Router examines level 1 route for best match
  There exist a match between192.168.1.2 & 192.168.1.0 / 24
  Router forwards packets out s0/0/0

## Slide 21: Routing Table Lookup Process
The process of matching
-1st there must be a match made between the parent route & destination IP
      -If a match is made then an attempt at finding a match between the destination IP and the child route is made.

## Slide 22: Routing Table Lookup Process
Finding a match between packet’s destination IP address and the next route in the routing table
-The figure shows a match between the destination IP of 192.168.1.0 and the level one IP of 192.168.1.0 / 24 then packet forwarded out s0/0/0

## Slide 23: Routing Table Lookup Process
Level 1 Parent & Level 2 Child Routes
Before level 2 child routes are examined
-There must be a match between classful level one parent route and destination IP address.

## Slide 24: Routing Table Lookup Process
After the match with parent route has been made Level 2 child routes will be examined for a match
-Route lookup process searches for child routes with a match with destination IP

## Slide 25: Routing Table Lookup Process
How a router finds a match with one of the level 2 child routes
-First router examines parent routes for a match
-If a match exists then:
        Child routes are examined
        Child route chosen is the one with the longest match

## Slide 26: Routing Table Lookup Process
Example: Route Lookup Process with VLSM
-The use of VLSM does not change the lookup process
-If there is a match between destination IP address and the level 1 parent route then
-Level 2 child routes will be searched

## Slide 27: Routing Behavior
Classful & classless routing protocols
Influence how routing table is populated
Classful & classless routing behaviors
Determines how routing table is searched after it is filled

## Slide 28: Routing Behavior
Classful Routing Behavior: no ip classless
What happens if there is not a match with any level 2 child routes of the parent?
-Router must determine if the routing behavior is classless or classful
-If router is utilizing classful routing behavior then
-Lookup process is terminated and packet is dropped

## Slide 29: Routing Behavior
Classful Routing Behavior – Search Process
An example of when classful routing behavior is in effect and why the router drops the Packet
  -The destination’s subnet mask is a /24 and none of the child routes left most bits match the first 24 bits. This means packet is dropped

## Slide 30: Routing Behavior
Classful Routing Behavior – Search Process
The reason why the router will not search beyond the child routes
        Originally networks were all classful
        This meant an organization could subnet a major network address and “enlighten” all the organization’s routers about the subnetting
        Therefore, if the subnet was not in the routing table, the subnet did not exist and packet was dropped

## Slide 31: Routing Behavior
ip Classless
Beginning with IOS 11.3, ip classless was configured by default
Classless routing behavior works for
-Discontiguous networks
And
-CIDR supernets

## Slide 32: Routing Behavior
Classless Routing Behavior: ip classless
Route lookup process when ip classless is in use
-If classless routing behavior in effect then
        Search level 1 routes
        Supernet routes Checked first
-If a match exists then forward packet
        Default routes Checked second
If there is no match or no default route then the
        Packet is dropped

## Slide 33: Routing Behavior
Classless Routing Behavior – Search Process
Router begins search process by finding a match between destination IP and parent route
After finding the above mentioned match, then there is a search of the child route

## Slide 34: Routing Behavior
Classless Routing Behavior – Search Process
If no match is found in child routes of previous slide then
Router continues to search the routing table for a match that may have fewer bits in the match

## Slide 35: Routing Behavior
Classful vs. Classless Routing Behavior
-It is recommended to use classless routing behavior
      Reason: so supernet and default routes can be used whenever needed

## Slide 36: Summary
Content/structure of a routing table
Routing table entries
-Directly connected networks
-Static route
-Dynamic routing protocols
Routing tables are hierarchical
-Level 1 route
Have a subnet mask that is less than or equal to classful subnet mask for the network address
-Level 2 route
These are subnets of a network address

## Slide 37: Summary
Routing table lookup process
Begins with examining level 1 routes for best match with packet’s destination IP
  If the best match = an ultimate route then
  -Packet is forwarded -Else-
  -Parent route is examined
  If parent route & destination IP match then Level 2 (child) routes are examined
  Level 2 route examination
  If a match between destination IP and child route found then Packet forwarded -Else
  If Router is using classful routing behavior then Packet is dropped -Else
  If router is using classless routing behavior then
  Router searches Level 1 supernet & default routes for a match
  If a match is found then Packet if forwarded -Else
  Packet is dropped

## Slide 38: Summary
Routing behaviors
-This refers to how a routing table is searched
Classful routing behavior
-Indicated by the use of the no ip classless command
-Router will not look beyond child routes for a lesser match
Classless routing behavior
-Indicated by the use of the ip classless command
-Router will look beyond child routes for a lesser match